## Slide 1: Servo-motor control using NI ELVIS Digital Systems Development Board
Hardware-Software Platforms: Project Presentation
DUFRANE Antoine (Antoine.DUFRANE@student.umons.ac.be)
FOTSO Mathieu (Mathieu.FOTSOTAGNE@student.umons.ac.be)
LEGER Louise (Louise.LEGER@student.umons.ac.be)

## Slide 2: Contents
Context
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
  Capacitive touch screen
Software operation

## Slide 3: Contents
Context
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
  Capacitive touch screen
Software operation

## Slide 4: Context
This tutorial takes place in the Hardware/Software Platforms lesson in first master in electrical engineering of the Faculty of Engineering of Mons
Goals:
To handle the Digital Systems Development Board of National Instrument and LabView
To control a servo-motor by using different interfaces
To understand the creation of VHDL code
In addition to this tutorial, a written report was created as well as a video presentation. Both can be found on GitHub.

## Slide 5: Contents
Context
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
  Capacitive touch screen
Software operation

## Slide 6: Software to install
LabView 2018
  http://www.ni.com/download/labview-development-system-2018/7407/en/
LabVIEW FPGA Module 2018
  http://www.ni.com/download/labview-fpga-module-2018/7351/en/
LabVIEW 2018 FPGA Module Xilinx Tools
  http://www.ni.com/download/labview-fpga-module-2018/7353/en/
DSDB Driver
  http://www.ni.com/download/digital-systems-development-board-driver-for-labview-2018/7441/en/

## Slide 7: DSDB installation
Insert the DSDB Board into the NI Elvis Board
Plug the board
  Connect the NI Elvis Board to the power supply
  Connect the UART port to the computer

## Slide 8: DSDB installation
LED “power”, “active” “PGOOD” should be on when plugging the board
Check that the JTAG position is selected
SD: code is written on an external SD card
QSPI: code is written on the memory of the board
JTAG: code is written on the volatile memory of the board

## Slide 9: Contents
Context
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
  Capacitive touch screen
Software operation

## Slide 10: Create a new project on LabView
Open LabView 2018
Click on “Create a project”
A new window will open
  Click on “empty project” then “finish”
A window “project explorer” will open
  Right click on “work station”
  New
  Targets and peripherals
A window “Add targets and peripherals” will open
  Tick “new target or new peripheral”
  Open “Digilent”
  Select “Digital Systems Development Board”
  Click on “OK”

## Slide 11: Create a new project on LabView
All ports of the board are now displayed
Right click on “FPGA Target: DSDB,…”
  New
  VI
Two new windows open
  Diagram window: where coding blocs will be positioned
  Front-side window: interface with the user

## Slide 12: Contents
Context
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
  Capacitive touch screen
Software operation

## Slide 13: Sending data on a digital port
Slide port “BB3_DiO0” (corresponding to a digital port) from the project explorer window to the diagram window
  Note : this port depend on the chosen port for the LED on the board

## Slide 14: Sending data on a digital port
Add a while loop
  Search for “while loop” on the research bar
  Make a square, creating a while loop
Add loop stop condition
  Search for “false constant”
  Connect it to the stop button of the while loop (red button)
    That way, the loop will never end

## Slide 15: Sending data on a digital port
Slide block “BTN0” from the project explorer window to the diagram window
  This block corresponds to the first button on the board
Connect the button to the digital port
  Select the output pin of the button and connect it to the input pin of the digital port

## Slide 16: Import the code on the board
In the diagram window, click on the white arrow (execute) on the top of the window
Save your project
In the “Select Compile Server” window
  Tick “Use the local compile server”
  OK
Compilation should be launched. This can take a few minutes

## Slide 17: Sending data on a digital port
You can now check the value when the button is pressed with a multimeter between “BB3_DiO0” and “GND”.
Connect a LED in series with a 220Ω resistor between “BB3_DiO0” and “GND”.
  The LED should now lights on when the button is pressed.

## Slide 18: Contents
Context
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
  Capacitive touch screen
Software operation

## Slide 19: Contents
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
    Connection of the servo-motor
    Control with user interface on computer
    Control with buttons on the board
  Capacitive touch screen

## Slide 20: Connection of the servo-motor
One servo-motor and three cables are needed
Connect the cables:
  The signal port to a digital port of the board (D0 here)
  “+” to 5V on the board
  “-” to the ground on the board

## Slide 21: Contents
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
    Connection of the servo-motor
    Control with user interface on computer
    Control with buttons on the board
  Capacitive touch screen

## Slide 22: Programming of the servo-motor
Slide port “BB3_DiO0” from the project explorer window to the diagram window
  Note : this port depend on the chosen port for the servo on the board

## Slide 23: Programming of the servo-motor
Add a while loop
  Search for “while loop” on the research bar
  Make a square, creating a while loop
Add loop stop condition
  Search for “false constant”
  Connect it to the stop button of the while loop (red button)
    That way, the loop will never end

## Slide 24: Programming of the servo-motor
Add a square wave for the PWM
  Right click in the diagram window in order to display functions
  Select “FPGA Math & Analysis
  Select “ Generation”
  Select “Square wave” and slide it in the while loop
Chose properties of the square wave
  Chose a frequency of 50 Hz and a Boolean data type

## Slide 25: Programming of the servo-motor
Connect the square wave to the digital port
  Right click on the digital port, select “change in writing” in order to transform it into an output instead of an input
  Select the square wave output port
  Connect it to the output pin of the digital port

## Slide 26: Programming of the servo-motor
Transform an angle into a duty cycle
  Knowing that to 0° correspond 2% and to 180° 11%, the line equation is:
  Implement this in the while loop
    Add, multiply and constant blocs can be found when right clicking in the while loop and selecting “Numeric”

## Slide 27: Programming of the servo-motor
Add the angle control
  Right click on the last port of the multiply bloc
  Select “create”
  Select “command”: a bloc should appear

## Slide 28: Programming of the servo-motor
Add an interface for the user
  Double click on the new bloc: this should open the front-side window
  Select the element with “0” and click right
  Select “replace”, “Numeric” and finally the kind of interface wanted. Here, a rotating button is chosen.

## Slide 29: Programming of the servo-motor
Adapt the button to the application
  Right click on the button: the properties window opens
  In scale: chose 180 for the maximum
  Click on “OK”

## Slide 30: Contents
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
    Connection of the servo-motor
    Control with user interface on computer
    Control with buttons on the board
  Capacitive touch screen

## Slide 31: Control of servo-motor angle with buttons on the board
The purpose of this test is to increase and decrease the angle of the servo-motor by pressing buttons on the board, and to display the value of the angle on the computer screen in LabView

## Slide 32: Control of servo-motor angle with buttons on the board
1: Previous blocs for PWM
2: Limitation of the mechanical servo position
3: Command of the servo by pressing buttons
1
2
3

## Slide 33: Test bench
This section consists of the verification of the code before
sending data to the servo. The control of the servo is made
by a PWM signal with a Duty Cycle between 2% and 12% at
50Hz.
For an angle of 0°:
= 2%

## Slide 34: Test bench
For an angle of 90°:
= 7%
For an angle of 180°:
= 11%

## Slide 35: Contents
Context
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
  Capacitive touch screen
Software operation

## Slide 36: Other examples
Other examples can be found on GitHub. For instance the utilisation of the capacitive touchscreen.
The classical example displays a circle when the screen is touched.

## Slide 37: Contents
Context
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  LED and buttons
  Servo-motor
  Capacitive touch screen
Software operation

## Slide 38: How does it work?
  LabView generates a report after the compilation
  All steps of the compilation can be found in this report
  Compiler = Vivado by Xilinx
  The programming is made using blocks which are interpreted in a VHDL code
  The VHDL pseudo-code of each block is accessible only during the compilation
  After this step all files are deleted

## Slide 39: How does it work?
Compilation report
Synthesizing modules, truth table, cell usage, optimization, …

## Slide 40: How does it work?
C:\NIFPGA\jobs
VHDL code for synthesizing in LabView

## Slide 41: Thanks for your attention !
DUFRANE Antoine (Antoine.DUFRANE@student.umons.ac.be)
FOTSO Mathieu (Mathieu.FOTSOTAGNE@student.umons.ac.be)
LEGER Louise (Louise.LEGER@student.umons.ac.be)